PERFORMANCE OF THE ANALOG DEVICES AD780BR   VOLTAGE REFERENCE AT CRYOGENIC TEMPERATURES

Test Report

Richard Patterson

NASA Glenn Research Center

&

Ahmad Hammoud

QSS Group, Inc.

NASA Glenn Research Center

Cleveland, Ohio

March 22, 2002

PERFORMANCE OF THE ANALOG DEVICES AD780BR

VOLTAGE REFERENCE AT CRYOGENIC TEMPERATURES

Background

The Analog Devices AD780 is an ultrahigh precision bandgap voltage reference that can provide a pin-programmable output of 2.5 V or 3.0 V from inputs between 4.0 V and 36 V.  It can be used to improve the performance of high-resolution analog-to-digital and digital-to-analog converters due to its capacitive-load driving capability. The device is specified for operation from –40 (C to +85 (C with low temperature drift and low output noise [1]. A temperature output pin provided on the AD780 allows the device to be configured as a temperature transducer while providing a stable output reference voltage. The output of the temperature transducer, which can be used to monitor changes in the system ambient temperature, varies linearly with temperature. The AD780BR device is capable of sourcing or sinking up to 10 mA and can be used in series or shunt mode, thus allowing positive or negative output voltages without external components. The performance of plastic-packaged devices (in this case an SOIC 8 pin plastic package) at low temperatures was investigated in this work.

Test Setup

A circuit board, populated with the AD780BR and few passive components, was designed and built for evaluation in the temperature range of +25 (C to –180 (C. The device was characterized at test temperatures of 25, 0, -40, -80, -100, -120, -140, -160 and -180 (C in a liquid nitrogen cooled environmental chamber.  At each test temperature, the device was allowed to soak for 15 minutes before measurements were made. Limited thermal cycle testing was also performed on the AD780BR. These tests consisted of subjecting the device to a total of ten thermal cycles between +90 (C and –125 (C at a temperature rate of 10 (C/min.  Device characterization was also performed at various temperatures after completion of the thermal cycling activity.

The device performance was evaluated in terms of its 2.5 V output voltage regulation and its temperature transducer output. These characteristics were obtained using input voltages of 4, 18, and 36 volts and at three load levels. Differing resistive loads were selected so that the load current ranged between 0 and 8.33 mA. The device is specified to source or sink up to 10 mA.

Results and Discussion

Figure 1 shows the deviation in the output voltage of the device with respect to its room temperature value. The data, which is shown as a function of temperature, is depicted for all input voltage and load level combinations. It can be seen that the reference output voltage remains within specifications (2.499 to 2.501 V) between temperatures of 25 (C to –40 (C.   Beyond –40 (C, however, the output voltage begins to decrease as the temperature is decreased. While this decrease in the output voltage is very minimal down to temperatures of -120 (C, it becomes more significant as the temperature is decreased further. In addition, the device exhibits unstable operation at the two extreme low temperatures; namely –160 (C and –180 (C. Instability was also observed at the test temperature of -140 (C only when an input voltage of 4 V is applied under no load condition. It is important to note that if the output specifications were broadened to cover a range of 2.495 V to 2.501 V, the device would be useful down to temperatures of  –120 (C.  Table I lists all the data obtained under the various test conditions. The operating points at which the output voltage went out of specification limits and device instability occurred are shown as shaded areas in Table I.

Figure 1. Deviation in the output voltage versus temperature at different test conditions.

The temperature sensor output of the AD780BR as a function of temperature is shown in Figure 2 for three different test conditions. It can be seen that for any selected input (supply) voltage, the transducer output is nearly linear with temperature for most of the range between 25 (C and –180 (C. The non-linearity seen at the extreme temperatures is due to the instability exhibited by the device, as was mentioned earlier. Data of the temperature sensor output is listed also in Table I.

Figure 2. Temperature pin output versus temperature at different test conditions.

Table I.  Results of low temperature evaluation of Analog Devices AD780BR voltage reference.

Input Voltage

(V)

Output

Current

(mA)

Temp

((C)

Output

Voltage

(V)

Temp

Voltage

| (V) |
| --- |
| 4 | 0 | 25 | 2.5001 | .559 |
| 18 | 0 | 25 | 2.5001 | .564 |
| 36 | 0 | 25 | 2.5001 | .567 |
| 4 | 1.78 | 25 | 2.5001 | .563 |
| 18 | 1.78 | 25 | 2.5001 | .572 |
| 36 | 1.78 | 25 | 2.5001 | .584 |
| 4 | 8.33 | 25 | 2.4996 | .562 |
| 18 | 8.33 | 25 | 2.4996 | .594 |
| 36 | 8.33 | 25 | 2.4996 | .633 |
| 4 | 0 | 0 | 2.5001 | .510 |
| 18 | 0 | 0 | 2.5001 | .514 |
| 36 | 0 | 0 | 2.5001 | .517 |
| 4 | 1.78 | 0 | 2.5001 | .513 |
| 18 | 1.78 | 0 | 2.5001 | .519 |
| 36 | 1.78 | 0 | 2.5001 | .529 |
| 4 | 8.33 | 0 | 2.4999 | .516 |
| 18 | 8.33 | 0 | 2.4999 | .541 |
| 36 | 8.33 | 0 | 2.4999 | .575 |
| 4 | 0 | -40 | 2.4998 | .432 |
| 18 | 0 | -40 | 2.4999 | .437 |
| 36 | 0 | -40 | 2.4999 | .441 |
| 4 | 1.78 | -40 | 2.4998 | .437 |
| 18 | 1.78 | -40 | 2.4999 | .444 |
| 36 | 1.78 | -40 | 2.5000 | .455 |
| 4 | 8.33 | -40 | 2.4994 | .439 |
| 18 | 8.33 | -40 | 2.4997 | .465 |
| 36 | 8.33 | -40 | 2.5000 | .500 |
| 4 | 0 | -80 | 2.4979 | .356 |
| 18 | 0 | -80 | 2.4980 | .359 |
| 36 | 0 | -80 | 2.4982 | .364 |
| 4 | 1.78 | -80 | 2.4981 | .361 |
| 18 | 1.78 | -80 | 2.4984 | .369 |
| 36 | 1.78 | -80 | 2.4986 | .379 |
| 4 | 8.33 | -80 | 2.4980 | .364 |
| 18 | 8.33 | -80 | 2.4988 | .390 |
| 36 | 8.33 | -80 | 2.4995 | .430 |
| 4 | 0 | -100 | 2.4973 | .321 |
| 18 | 0 | -100 | 2.4974 | .342 |
| 36 | 0 | -100 | 2.4976 | .330 |
| 4 | 1.78 | -100 | 2.4978 | .324 |
| 18 | 1.78 | -100 | 2.4976 | .331 |
| 36 | 1.78 | -100 | 2.4980 | .343 |
| 4 | 8.33 | -100 | 2.4971 | .327 |

Input Voltage

(V)

Output

Current

(mA)

Temp

((C)

Output

Voltage

(V)

Temp

Voltage

| (V) |
| --- |
| 18 | 8.33 | -100 | 2.4980 | .353 |
| 36 | 8.33 | -100 | 2.4989 | .392 |
| 4 | 0 | -120 | 2.4955 | .285 |
| 18 | 0 | -120 | 2.4958 | .289 |
| 36 | 0 | -120 | 2.4960 | .292 |
| 4 | 1.78 | -120 | 2.4955 | .286 |
| 18 | 1.78 | -120 | 2.4961 | .295 |
| 36 | 1.78 | -120 | 2.4967 | .306 |
| 4 | 8.33 | -120 | 2.4955 | .290 |
| 18 | 8.33 | -120 | 2.4970 | .317 |
| 36 | 8.33 | -120 | 2.4984 | .355 |
| 4 | 0 | -140 | 2.4981 | .252 |
| 18 | 0 | -140 | 2.4982 | .254 |
| 36 | 0 | -140 | 2.4981 | .258 |
| 4 | 1.78 | -140 | 2.4973 | .251 |
| 18 | 1.78 | -140 | 2.4976 | .260 |
| 36 | 1.78 | -140 | 2.4976 | .272 |
| 4 | 8.33 | -140 | 1.9386 | .037 |
| 18 | 8.33 | -140 | 2.4966 | .283 |
| 36 | 8.33 | -140 | 2.4976 | .321 |
| 4 | 0 | -160 | 2.4962 | .215 |
| 18 | 0 | -160 | 2.4965 | .219 |
| 36 | 0 | -160 | 2.4961 | .222 |
| 4 | 1.78 | -160 | 2.4060 | .215 |
| 18 | 1.78 | -160 | 2.4959 | .225 |
| 36 | 1.78 | -160 | 2.4956 | .235 |
| 4 | 8.33 | -160 |
| 18 | 8.33 | -160 | 2.0040 | .040 |
| 36 | 8.33 | -160 | 2.4967 | .286 |
| 4 | 0 | -180 | 2.4946 | .180 |
| 18 | 0 | -180 | 2.6759 | .259 |
| 36 | 0 | -180 | 2.6178 | .245 |
| 4 | 1.78 | -180 | 1.5670 | 0 |
| 18 | 1.78 | -180 | 2.5824 | .226 |
| 36 | 1.78 | -180 | 2.5170 | .209 |
| 4 | 8.33 | -180 |
| 18 | 8.33 | -180 | 1.2795 | 0 |
| 36 | 8.33 | -180 | 2.4951 | .252 |

|  | Voltage out of specifications |
| --- | --- |
|  | Unstable operation |

After this basic characterization with temperature, the device was subjected, as mentioned earlier, to ten thermal cycles between +90 (C and – 125 (C. Measurements of the device parameters were then followed at various temperatures. The post-thermal cycling data is listed in Table II. The results obtained were in good agreement to those obtained prior to the thermal cycling. Hence, it can be concluded that this limited thermal cycling had no significant effect on the characteristics of the AD780BR voltage reference.

Table II.  Post-thermal cycling results of Analog Devices AD780BR voltage reference.

Input Voltage

(V)

Output

Current

(mA)

Temp

((C)

Output

Voltage

(V)

Temp

Voltage

| (V) |
| --- |
| 4 | 0 | 25 | 2.5006 | .558 |
| 18 | 0 | 25 | 2.5007 | .561 |
| 36 | 0 | 25 | 2.5006 | .574 |
| 4 | 1.78 | 25 | 2.5005 | .559 |
| 18 | 1.78 | 25 | 2.5005 | .567 |
| 36 | 1.78 | 25 | 2.5005 | .603 |
| 4 | 8.33 | 25 | 2.5000 | .562 |
| 18 | 8.33 | 25 | 2.5000 | .594 |
| 36 | 8.33 | 25 | 2.5002 | .651 |
| 4 | 0 | -40 | 2.4999 | .432 |
| 18 | 0 | -40 | 2.5001 | .441 |
| 36 | 0 | -40 | 2.5001 | .442 |
| 4 | 1.78 | -40 | 2.4999 | .435 |
| 18 | 1.78 | -40 | 2.5000 | .443 |
| 36 | 1.78 | -40 | 2.5000 | .450 |
| 4 | 8.33 | -40 | 2.4995 | .435 |
| 18 | 8.33 | -40 | 2.4998 | .461 |
| 36 | 8.33 | -40 | 2.5000 | .502 |
| 4 | 0 | -120 | 2.4945 | .285 |
| 18 | 0 | -120 | 2.4948 | .288 |
| 36 | 0 | -120 | 2.4952 | .294 |
| 4 | 1.78 | -120 | 2.4945 | .285 |
| 18 | 1.78 | -120 | 2.4950 | .292 |
| 36 | 1.78 | -120 | 2.4958 | .305 |
| 4 | 8.33 | -120 | 2.4944 | .289 |
| 18 | 8.33 | -120 | 2.4962 | .318 |
| 36 | 8.33 | -120 | 2.4980 | .357 |

Input Voltage

(V)

Output

Current

(mA)

Temp

((C)

Output

Voltage

(V)

Temp

Voltage

| (V) |
| --- |
| 4 | 0 | -140 | 2.4937 | .249 |
| 18 | 0 | -140 | 2.4938 | .255 |
| 36 | 0 | -140 | 2.4938 | .259 |
| 4 | 1.78 | -140 | 2.4936 | .254 |
| 18 | 1.78 | -140 | 2.4939 | .262 |
| 36 | 1.78 | -140 | 2.4942 | .274 |
| 4 | 8.33 | -140 | 1.9758 | .060 |
| 18 | 8.33 | -140 | 2.4944 | .283 |
| 36 | 8.33 | -140 | 2.4965 | .322 |
| 4 | 0 | -160 | 2.4944 | .217 |
| 18 | 0 | -160 | 2.4945 | .220 |
| 36 | 0 | -160 | 2.4942 | .225 |
| 4 | 1.78 | -160 | 2.4941 | .218 |
| 18 | 1.78 | -160 | 2.4940 | .226 |
| 36 | 1.78 | -160 | 2.4939 | .238 |
| 4 | 8.33 | -160 | 1.4200 | .000 |
| 18 | 8.33 | -160 | 1.9000 | .064 |
| 36 | 8.33 | -160 | 2.4948 | .286 |
| 4 | 0 | -180 | 2.4963 | .18 |
| 18 | 0 | -180 | 2.6200 | .244 |
| 36 | 0 | -180 | 2.5700 | .229 |
| 4 | 1.78 | -180 | 2.1200 | .049 |
| 18 | 1.78 | -180 | 2.5433 | .217 |
| 36 | 1.78 | -180 | 2.5040 | .209 |
| 4 | 8.33 | -180 | 0.6170 | 0 |
| 18 | 8.33 | -180 | 1.3000 | 0 |
| 36 | 8.33 | -180 | 2.4939 | .251 |

|  | Voltage out of specifications |
| --- | --- |
|  | Unstable operation |

Conclusion

The Analog Devices AD780BR is a commercial-grade, ultrahigh precision voltage reference device rated for –40 (C to +85 (C operation.  The SOIC 8 pin plastic package device was evaluated for potential use in low temperature applications down to –180 (C with a 2.5 V output reference voltage.  The device was characterized in terms of its output regulation and temperature sensing output in the temperature range of +25 (C to -180 (C.  While the device performed well with respect to output voltage regulation with temperature down to –40 (C, the manufacturer’s specified low temperature rating, it does have potential use down to –120 (C if the acceptable output is broadened to cover the range of 2.495 V to 2.501 V.  With an input voltage level of 36 V, the acceptable output just mentioned can be obtained down to –160 (C. The output of the built-in temperature sensor worked well and was linear with temperature for most of the test range between 25 (C and –180 (C. No effect was observed in the operational characteristics of the device due to the applied limited thermal cycling. Further testing and long-term cycling are needed, however, to fully characterize the performance of the device and to determine its reliability for operation in low temperature environments.

References

1. Analog Devices AD780 High Precision Reference Data Sheet, Rev. B.

Acknowledgments

This work was performed under the NASA Glenn Research Center GESS Contract # NAS3-00145. Support was also provided from the NASA Electronic Parts and Packaging (NEPP) Program, EPAR Task “Electronics for Extreme Environments”.